## Slide 1
（信息与）通信技术（基础）
Module 4: Analog Modulation
王超
电子与信息工程学院 - 信息与通信工程系
教授/博士生导师
Email: chaowang@tongji.edu.cn

## Slide 2
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 3
Modulation
Modulation refers to the modification of one signal’s characteristics in sympathy with another signal.
Analog modulation: Modulation of a carrier by utilizing a source baseband analog signal.
Carrier: A deterministic periodic waveform, e.g.:
where is amplitude, is angular frequency, and is initial phase.
Modulation enables a parameter of the carrier, , to vary with the source signal, , i.e. the value of is represented by the value of a parameter of .
Modulator
Modulated
signal s(t)
Modulating
signal m(t)

## Slide 4
Modulation
The source signal is called modulating signal, the carrier after being modulated, , is called modulated signal, and the device for modulation is called modulator.
Purposes of modulation
  To realize frequency spectrum movement: Accommodating the requirement of channel transmission or conducting multi-channel transmission
  To improve the anti-jamming ability
Classification
  Linear modulation: The frequency spectrum structure of modulated signal remains the same as that of modulating signal.
  Nonlinear modulation (also called angle modulation): The frequency spectrum structures of modulated and modulating signals are different (new frequency components are generated)

## Slide 5
Linear Modulation
Let the carrier signal be , where is frequency (Hz).
The principle model of a linear modulator is to pass the multiplication of and , i.e.
through a bandpass filter with transfer function .
The characteristic of the bandpass filter may have different designs, resulting in different modulation modes.

H(f)
s(t)
Modulated signal
s(t)
Modulating
signal
m(t)
Acos0t

## Slide 6
Linear Modulation
Assume to be an energy signal with frequency spectral density , i.e. . We have:
The signal is cosinusoidal wave, whose amplitude is proportional to , i.e. the amplitude of the carrier waveform is modulated.
is the displacement result of .
  (a) Frequency spectral density of input signal
S (f)
f0
f
-f0
0
M(f)
f
0
  (b) Frequency spectral density
  of output signal

## Slide 7
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 8
Amplitude Modulation (AM)
Let ,
  1 can be seen as the DC component, is the AC component
  The maximum of is called modulation index ()
The output of the multiplier is
m(t)
1
0
1+m(t)
1
0
1+m(t)

## Slide 9
Spectrum of AM Signals
The frequency spectral density contains discrete carrier components
The bandwidth is , where is the highest frequency of the baseband signal
  Spectral efficiency of AM is low
Most part of the power is occupied by the carrier signal, which does not contain information
  Power efficiency of AM is low.
m'(t)
s(t)
c(t)
A
-A
t
t
t



M’(f)
C(f)
fm
-fm
f0
-f0
2fm
S (f)
2fm
-f0
f0
f
f
f

## Slide 10
Exercise
Let the modulated signal , calculate, when (or 100%) and (or ), the ratio of the sum of the two sideband powers to the total modulated signal power.

## Slide 11
Demodulation of AM Signals
An envelope detector is normally used to restore the original modulating signal.
The envelope detector consists of a rectifier and a low-pass filter.
A capacitor is used to separate the DC component
Rectifier
Low-pass filter
Envelope detector

## Slide 12
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 13
Double-sideband Modulation (DSB)
When the modulating signal does not contain DC component, there is no carrier in the output signal of the multiplier.
This kind of modulation is called DSB, since its frequency spectrum contains two sidebands.
The two sidebands are called upper-sideband and lower-sideband respectively, which contain the same information.
The power efficiency of DSB signal is much higher than AM signal. Their spectrum efficiencies are the same.
M(f)
f
0
f0
0
-f0
f
S(f)
  (a) Frequency spectral density of modulating signal
Upper-sideband
  (b) Frequency spectral density
  of modulated signal
Upper-sideband
Lower-sideband

## Slide 14
Demodulation of DSB Signals
Envelope detector is no longer applicable, since the envelope of DSB signal is not the same as the modulating signal.
A coherent demodulator should be used.
Assume that the received DSB signal is , then
The output of the low-pass filter is .
Baseband signal
m(t)
Received signal
s(t)
cos0t
r(t)

LPF

## Slide 15
Demodulation of DSB Signals
  The output signal equals , only if the local carrier has no frequency and phase error.
  If the frequency and phase of the local carrier have errors, i.e. assume its expression is , we have
output: .
DSB signal can save transmitting power, but the receiving circuit will be rather complicated.
Notes:   Pros and cons:

## Slide 16
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 17
Single-sideband Modulation (SSB)
The two sidebands of the DSB signal contains the same information, which results in inefficient use of channel.
SSB transmits only one sideband of the DSB signal.
The filter
Both power efficiency and spectrum efficiency of SSB signals are higher than AM and DSB signals.
(b) Upper-sideband filter characteristic and signal frequency spectrum
f0
0
f
-f0
0
f
f0
-f0
HH(f)
HH(f)
S(f)
Upper-sideband
Upper-sideband
(c) Lower-sideband filter characteristic and signal frequency spectrum
-f0
f0
f
HL(f)
S(f)
Lower-sideband
(a) Signal frequency spectrum before filtering
Upper-sideband
S(f)
Upper-sideband
Lower-sideband
17

## Slide 18
Demodulation of SSB Signals
Demodulation: A carrier is multiplied to the received signal
Time-domain and frequency-domain operations
The multiplication of carrier with the received signal is equivalent to the convolution of the carrier frequency spectrum with the signal frequency spectrum in the frequency domain.
Notes:   Pros and cons:

## Slide 19
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 20
Vestigial Sideband Modulation (VSB)
Despite the high power and spectrum efficiency, SSB requires high system complexity
  The local carrier at the demodulator must have the same frequency and phase as that in the transmitter
  The modulator should have a very high-quality filter to attain SSB from DSB or AM signals.
  VSB allows the modulating signal to contain very low frequency and DC components

H(f)
s(t)
Modulated signal
s(t)
Modulating
signal
m(t)
Acos0t
Baseband signal
m(t)
Received signal
s(t)
cos0t
r(t)

LPF

## Slide 21
Vestigial Sideband Modulation (VSB)
Frequency spectrum expression of the output signal of the multiplier is
After being filtered, the frequency spectrum of VSB signal is:
What condition should be satisfied, to realize demodulation without distortion?
The frequency spectrum of the output signal of the multiplier at the demodulator, , is

## Slide 22
Vestigial Sideband Modulation (VSB)
The output demodulated signal after the low-pass filter is
Transmission without distortion requires
where is a constant.
Since is the frequency spectral density function of the baseband modulating signal, let its highest frequency component be , i.e. when .
We have

## Slide 23
Vestigial Sideband Modulation (VSB)
H(f + f0)
-(f0+fm)
0
0
0
0
f
f
f
f0
-f0
f0+fm
-2f0
2f0
-2f0
2f0
fm
-fm
fm
f
H(f)
H(f - f0)
H(f + f0) + H(f – f0)

## Slide 24
Vestigial Sideband Modulation (VSB)
The cut-off characteristic of the filter is complementary symmetry with respect to the carrier frequency .
In addition to the whole frequency spectrum of SSB signal, a part of the carrier frequency component and a small part of another sideband frequency spectrum are reserved in the frequency spectrum of VSB modulated signal.
The filter in the modulator can be easily manufactured.
The main disadvantage is that the occupied frequency band is a little wider than that of the SSB signal.

## Slide 25
CONTENTS
目录
Modulation
Amplitude Modulation (AM)
Double-sideband Modulation (DSB)
Single-sideband Modulation (SSB)
Vestigial Sideband Modulation (VSB)
Angle Modulation

## Slide 26
Nonlinear Modulation
Nonlinear modulation is also called angle modulation, which enables frequency and phase of the carrier to vary with the modulating signal.
Let a carrier signal be expressed as
where is the instantaneous phase.
After being modulated, the signal’s instantaneous frequency becomes a function of time, i.e.
Equivalently
Angle modulation: varies with the modulating signal .

## Slide 27
Phase Modulation (PM)
Phase modulation: Phase linearly varies with , i.e.
where is a constant.
The modulated signal can be expressed as
The instantaneous frequency of the modulated signal is
The instantaneous frequency in phase modulation varies with the derivative of the modulating signal.

## Slide 28
Frequency Modulation (FM)
Frequency modulation: Instantaneous frequency linearly varies with the modulating signal, i.e.
where is a constant.
The phase of the modulated signal is:
The modulated signal is

## Slide 29
PM and FM Signals
Frequency modulation
Phase modulation

## Slide 30
Exercise
What are the pros and cons of FM and PM, compared with linear modulation methods?

## Slide 31
Summary
Analog modulation can be classified as linear modulation and nonlinear modulation.
Frequency spectrum structure of a linearly modulated signal is the displacement of that of the modulating signal.
Linear modulation includes AM, DSB, SSB, and VSB.
Nonlinear modulation is also called angle modulation, including frequency modulation and phase modulation.
Frequency spectrum structure of a non-linearly modulated signal is different from that of the modulating signal.

## Slide 32
Thank You!